## Slide 1: Eut+ Project
Ravindu Buddhila Danthasinghe
Mridul Mukherjee
Menelaos Menelaou
Marios Pirikki

## Slide 2: Power Systems Planning end-term assignment
Overview:
This project is to investigate the connection of distributed energy resources (DER) into the distribution grid. It is split into three parts:
Scenario-based analysis, separate for the MV and LV level
Time series analysis, combined for MV and LV level
Optimization using innovative planning and operation schemes

## Slide 3: Network
MV LEVEL :
LV LEVEL :

## Slide 4
Figure 1: Single-Line Diagram of the MV network [1].
Figure 2: Single-Line Diagram of the LV network [1].

## Slide 5: Scenario-based analysis
What extreme scenarios must be analysed before deciding if the connection of DER is permissible?
Testing according to DIN EN 50160: −
Maximum load & minimum generation at all voltage levels.
Minimum load 1) & maximum generation at all voltage levels.
1) Value for the load depends on the times, when maximum DER feed-in occurs (e.g. for PV between 10 am and 4 pm)
What tap-changer position (set-point value for voltage regulation on MV side) should be assumed for the HV/MV transformer depending on the scenario?
Maximum load & minimum generation at all voltage levels, minimum tapping (within control range) at HV / MV transformer.
Minimum load 1) & maximum generation at all voltage levels, maximum tapping (within control range) at HV/MV transformer.

## Slide 6
What is the maximum permissible voltage rise (in % of nominal voltage) for the MV and LV level during normal operation? How does this threshold change during n-1 contingency conditions?
Testing according to technical connection rules during normal conditions: −
MV level (bdew): voltage change when all DER are connected (compared to the case without any DER)
LV level (VDE AR 4100 and 4105): voltage change when all DER are connected
During normal operation (continuous voltage fluctuation)
Maximum voltage deviation at PCC (Point of Common Coupling)
− LV: -5% to +10%
− MV: -5% to +5% Defined for 95% of the time, measured over one week
During fault conditions (n-1 case, single outage):
− LV: -8% to +10%
− MV: -10% to +10%
After reactive actions (e.g., stepping of on-load tap-changer):
− MV: -8% to +8%

## Slide 7
What is the maximum permissible line loading under normal conditions for the MV and LV level?
Testing according to technical connection rules:
− Maximum load & minimum generation at all voltage levels, minimum tapping (within control range) at HV / MV transformer
− Minimum load 1) & maximum generation at all voltage levels In both cases, minimum tapping at HV / MV transformer
1) Value for the load depends on the times, when maximum DER feed-in occurs (e.g. for PV between 10 am and 4 pm).
For the current limits, the maximum steady-state loading is limited to 100 % of the long-term assets capacity. Some DSOs make exceptions, e.g., allowing a temporarily loading of 130 % of maximum steady-state loading for MV/LV stations.

## Slide 8
Based on the results for high load conditions, is the network n-1 secure? Which measures would you recommend for ensuring n-1 security?
For LV high load, low DER condition, it is not n-1 secure. We got line 9 as critical node.
Measures: Add a parallel line || Add parallel source feed in the system
Repeat the power flow calculation for light load, very high PV conditions. What difference do you notice?
More bus voltage increment because we have light load but more DER gen.
Extra DER gen. is feed to all grid systems (HV, MV, LV).
Compare the voltage drop / voltage rise with the permissible bandwidth. Is the network well designed?
During normal operation (continuous voltage fluctuation)
Maximum voltage deviation at PCC (Point of Common Coupling)
− LV: -5% to +10%
− MV: -5% to +5% Defined for 95% of the time, measured over one week .
The MV network is not well-defined while for high load low DER gen. we have from (Bus 3 – Bus 11) – min bus voltage < 0.95 p.u. and for low load high DER gen. we have from (Bus 3 – Bus 11) – max bus voltage > 1.05 p.u.
The LV network is not well-defined while for high load low DER gen. we have from (Bus 6 – Bus 19) – min bus voltage < 0.95 p.u.

## Slide 9: Results
Maximum load & minimum generation - MV

## Slide 10: Results
Minimum load & maximum generation - MV

## Slide 11: Results
Maximum load & minimum generation - LV

## Slide 12: Results
Minimum load & maximum generation - LV

## Slide 13
Which annual consumptions is assumed for the H0 load profile? How do you scale the profile for different levels of consumption?
Scaling - We divide all the load with the max load of all time.
Annual Consumption was assumed to be 1000KWh.
What is the morning and evening peak in consumption?
H0 load profile --- Morning peak --- > 173.1 W Evening peak --- > 213.2
G0 load profile --- Morning peak --- > 200 W Evening peak --- > 178.5
In which time of the year do you expect the peak household consumption? Is this the same for all countries, or rather specific to Germany?
- Winter. During the winter due to the heavy electrical usage (like heaters) it shows the maximum peak household consumption
- Depend on the climate

## Slide 14: Time Series Analysis Without DER
Weekday in Summer: Residential Case (H0)
Maximum, mean, and minimum voltage of the buses at MV voltage level
Maximum, mean, and minimum voltage of the buses at LV voltage level
Results

## Slide 15
Mean and maximum line loading over time
Results

## Slide 16
Sunday in Spring : Residential Case (H0)
Results
Maximum, mean, and minimum voltage of the buses at MV voltage level
Maximum, mean, and minimum voltage of the buses at LV voltage level

## Slide 17
Mean and maximum line loading over time
Results

## Slide 18
Maximum, mean, and minimum voltage of the buses at MV voltage level
Maximum, mean, and minimum voltage of the buses at LV voltage level
Saturday in Winter: Residential Case (H0)
Results

## Slide 19
Mean and maximum line loading over time
Results

## Slide 20
Maximum, mean, and minimum voltage of the buses at MV voltage level
Maximum, mean, and minimum voltage of the buses at LV voltage level
Weekday in Summer: Commercial Case (G0)
Results

## Slide 21
Mean and maximum line loading over time
Results

## Slide 22
Maximum, mean, and minimum voltage of the buses at MV voltage level
Maximum, mean, and minimum voltage of the buses at LV voltage level
Results
Sunday in Spring : Commercial Case (G0)

## Slide 23
Mean and maximum line loading over time
Results

## Slide 24
Maximum, mean, and minimum voltage of the buses at MV voltage level
Maximum, mean, and minimum voltage of the buses at LV voltage level
Results
Saturday in Winter : Commercial Case (G0)

## Slide 25
Mean and maximum line loading over time
Results

## Slide 26: Time Series Analysis with DER (Active power)
Maximum, mean, and minimum voltage of the buses at MV voltage level
Maximum, mean, and minimum voltage of the buses at LV voltage level
Weekday in Summer: Residential Case (H0)
Results

## Slide 27
Mean and maximum line loading over time
Results

## Slide 28
Maximum, mean, and minimum voltage of the buses at MV voltage level
Maximum, mean, and minimum voltage of the buses at LV voltage level
Saturday in Winter: Residential Case (H0)
Results

## Slide 29
Mean and maximum line loading over time
Results

## Slide 30
Maximum, mean, and minimum voltage of the buses at MV voltage level
Maximum, mean, and minimum voltage of the buses at LV voltage level
Sunday in Spring : Residential Case (H0)
Results

## Slide 31
Mean and maximum line loading over time
Results

## Slide 32
Maximum, mean, and minimum voltage of the buses at MV voltage level
Maximum, mean, and minimum voltage of the buses at LV voltage level
Weekday in Summer: Commercial Case (G0)
Results

## Slide 33
Mean and maximum line loading over time
Results

## Slide 34
Maximum, mean, and minimum voltage of the buses at MV voltage level
Maximum, mean, and minimum voltage of the buses at LV voltage level
Results
Saturday in Winter : Commercial Case (G0)

## Slide 35
Mean and maximum line loading over time
Results

## Slide 36
maximum, mean, and minimum voltage of the buses at MV voltage level
maximum, mean, and minimum voltage of the buses at LV voltage level
Results
Sunday in Spring : Commercial Case (G0)

## Slide 37
Mean and maximum line loading over time
Results

## Slide 38
Compare the maximum voltage drop/rise in the MV and LV network as well as the maximum line loading to the results from section 3. Which approach (scenario-based or time series) yields more onerous results?
Since we did not use the time series analysis more onerous is scenario-based analysis. We found out that the values for bus voltages are exceeding the permissible limits in Scenario based analysis.
Exercise 5
Network | Measurements |  | Scenario MV |  | Scenario LV |  | Scenario Combined | Time Series |  |  |  |  | 
 |  |  | High load, low DER gen. | Low load high DER gen. | High load, low DER gen. | Low load high DER gen. |  | H0 |  |  | G0 |  | 
 |  |  |  |  |  |  |  | Sum | Win | Spr | Sum | Win | Spr
MV | Bus Voltage | min | 0.902 | 1.02 |  |  | 0.902 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99
 |  | max | 1.03 | 1.06 |  |  | 1.06 | 1.03 | 1.03 | 1.03 | 1.03 | 1.03 | 1.03
 |  | mean | 0.937 | 1.04 |  |  | 0.99 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00
 | Line Loading | max | 99.88 | 64.30 |  |  | 99.98 | 89.4 | 115 | 115 | 94.2 | 116 | 47
 |  | mean | 27.44 | 17.58 |  |  | 22.51 | 17.3 | 20.8 | 20.1 | 18.8 | 19.4 | 12.2
LV | Bus Voltage | min |  |  | 0.91 | 1.0 | 0.91 | 0.97 | 0.92 | 0.93 | 0.94 | 0.92 | 0.97
 |  | max |  |  | 1.0 | 1.04 | 1.04 | 1.02 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99
 |  | mean |  |  | 0.94 | 1.02 | 0.98 | 0.99 | 0.97 | 0.97 | 0.97 | 0.97 | 0.98
 | Line Loading | max |  |  | 32.52 | 22.53 | 32.52 | 23.6 | 31 | 27.3 | 19 | 30.8 | 12.8
 |  | mean |  |  | 18.83 | 18.83 | 18.83 | 5.06 | 7.6 | 6.7 | 5.2 | 7.13 | 3.5